## Slide 1
AVR with Ascending Aortic and Arch Replacement under Circulatory Arrest
Sydney Lias
CVP 611 Clinical Applications II
7/15/2026

## Slide 2
Abstract
Case
Combined mechanical aortic valve replacement, ascending aortic grafting and subaortic membrane resection. Femoral and axillary cannulation enabled CPB cooling to 28 °C before the chest incision.
Result
Reported separation from bypass was successful. CPB time was 100 minutes, aortic cross-clamp time 55 minutes and circulatory arrest time 12 minutes.
Central lesson
Peripheral access created a controlled path to opening the chest by cooling, cerebral protection and definitive repair.
2

## Slide 3
Background of Patient
The patient is a 55-year-old woman with a complex congenital and surgical cardiac history, including prior ventricular septal defect (VSD) repair, aortic valve repair, septal myectomy, and subaortic membrane resection. She later developed recurrent subaortic membrane formation, severe torrential aortic insufficiency, and a 5-cm ascending aortic aneurysm. She presented with worsening shortness of breath and fatigue, prompting evaluation for redo cardiac surgery. Preoperative imaging demonstrated preserved left ventricular systolic function, a heavily calcified bicuspid aortic valve, ascending aorta stuck to the back of the sternum, and no obstructive coronary artery disease.
3

## Slide 4
Three lesions were addressed through one arrested-heart strategy
01
Aortic valve
Mechanical AVR restores competent valvular outflow. Mechanical prostheses generally require lifelong Warfarin for anticoagulation.
02
Ascending aorta
The diseased ascending segment is excised and replaced with a vascular graft along with the repair of the base of the subclavian
03
Subaortic membrane
A fixed fibrous ridge below the valve is removed through the aortic route to relieve LV outflow tract obstruction; recurrence surveillance remains important as this can reoccur.
Background: 2021 ESC/EACTS valve guideline; 2022 ACC/AHA aortic guideline; subaortic stenosis literature.
4

## Slide 5
Circulatory arrest trades operative access for time-limited ischemic risk
Stopping systemic flow creates a bloodless field for open distal aortic reconstruction. Protection depends on lowering metabolic demand and maintaining cerebral perfusion whenever anatomy permits.
28 °C
moderate hypothermia target reported in this case
Protection stack
Systemic cooling before arrest
Antegrade cerebral perfusion (ACP)
Neuromonitoring and pressure/flow targets per protocol
Shortest feasible no-flow intervals
Guideline context: 2022 ACC/AHA Aortic Disease; 2024 EACTS/EACTAIC/EBCP CPB.
5

## Slide 6
Femoral access supported systemic CPB; Axillary access enabled antegrade brain flow
Femoral cannulation
Rapid peripheral route for venous drainage using a 25F Medtronic Biomedicaus cannula.
Primary role in this case
Whole-body bypass and cooling
Axillary cannulation
Antegrade arterial access that can continue directed cerebral perfusion when distal systemic flow is stopped using a 8mm dacron graft connected to a 3/8 tubing.
Primary role in this case
Whole – body bypass and ACP during aortic reconstruction
dual arterial strategy
6

## Slide 7
Bypass and cooling were established before the sternotomy
1
Cannulate
Femoral and axillary access established before chest incision.
2
Anticoagulate
Systemic heparinization before CPB using 47,000 units of Heparin and 10,000 in prime: ACT reached 1005.
3
Initiate CPB
Reported full flow of 3.4 L/min during the initiations with a BSA of 1.87 m2.
4
Cool
Core temperature reduced on the initiation of bypass to 28 °C core temperature before skin incision.
7

## Slide 8
Sternotomy converted the plan from controlled cooling to active blood conservation
Trigger
After skin incision and median sternotomy, bleeding increased once the chest was opened.
Perfusion response
3
field suckers
~1 L/min each
8

## Slide 9
Cardioplegia preceded selective brain-only perfusion
Cross-clamp
Aortic cross-clamp applied
Cardioplegia
1 L retrograde of 25 mEq of potassium and 8 mEq of cardioplegia additive of Magnesium and Adenosine dose reported
ACP
Systemic flow reduced to 10 mL/kg/min with a flow of 700 mL; brain-only antegrade perfusion for 12 minues
9

## Slide 10
Aortic grafting required a brief interruption of cerebral flow
Ascending and Aortic arch graft
The ascending aorta was opened/resected and reconstructed with a vascular 28 mm Gelweace Terumo graft and the arch was replace with the same graft under arrest with ACP. NIRS went down 5% from baseline and MAP was reading 34.
Right subclavian base
This case had an instance of “zero cerebral flow” for 6 minutes during repair at the base of the right subclavian artery. NIRS went down 18% from baseline.
Flow restored
After completion of the critical distal repair, perfusion returned from selective cerebral flow to full-body flow of 4.27 L.
10

## Slide 11
Full-body perfusion supported valve replacement, rewarming and separation from CPB
1
Restore systemic flow and start to re-warm to 37 degrees Celsius
2
Resect subaortic membrane
3
Implant mechanical aortic valve using a 25mm St. Jude mechanical valve
4
Rewarm and de-air using the Root Vent and LV Sump on 1 liter each
5
Wean successfully
11

## Slide 12
The operative timeline concentrated risk into a 20-minute arrest window
TOTAL CPB
100 min
Clamp
55
min
Arrest
12
min
Cannulation → full flow → cooling → incision/sternotomy → clamp/cardioplegia → ACP/arrest → graft repair → full-body flow → AVR → wean
12

## Slide 13
The reported endpoints show efficient separation despite complex flow transitions
CARDIOPULMONARY BYPASS
100 min
AORTIC CROSS-CLAMP
55 min
CIRCULATORY ARREST
12 min
Key perfusion lesson
Peripheral cannulation before incision created a margin for controlled cooling, while axillary access preserved an antegrade cerebral route during open aortic work.
13

## Slide 14
References:
Isselbacher, E. M., Preventza, O., Black, J. H., III, et al. (2022). 2022 ACC/AHA guideline for the diagnosis and management of aortic disease. *Journal of the American College of Cardiology, 80*(24), e223–e393. https://doi.org/10.1016/j.jacc.2022.08.004
Vahanian, A., Beyersdorf, F., Praz, F., et al. (2022). 2021 ESC/EACTS guidelines for the management of valvular heart disease. *European Heart Journal, 43*(7), 561–632. https://doi.org/10.1093/eurheartj/ehab395
Wahba, A., Kunst, G., De Somer, F., et al. (2025). 2024 EACTS/EACTAIC/EBCP guidelines on cardiopulmonary bypass in adult cardiac surgery. *European Journal of Cardio-Thoracic Surgery, 67*(2), ezae354. https://doi.org/10.1093/ejcts/ezae354